# Align Sample
## Horizontal
Analog to the other scans, align in the middle of the preview window
## Vertical
- Top of the Sample Holder to the Bottom of the Camera window (Note Position e.g. as '-7850')
- Top of the Sample to the Top of the Camera Window, so you have the full sample inside X Camera Windows (Note Position e.g. as '150')
# Stacked scan
- Set Name, Angle (-180:180) and Number of Projections in the ControlPanel
- Use the Terminal of 'x02da-cons-2' to start the stacked scan with the following command:
/work/sls/bin/stacked_scan.py -t -7850 150 2048 10 1
- Parameterlist:
  - '-t' just tests all Parameters and doesn't run anything. Use this to double-check the positions in the preview
  - Pos1 (-7850) and Pos2 (150) are the Y-Positions of the Sample at the top and bottom, in MicroMeters
  - '2048' Number of Lines in Projection (in the camera window). A small overlap is built into the script, so you can use the 'real' number
  - '10' Magnification
  - '1' Binning